Material Safety Data Sheet: Specifying Respiratory Filter Type

Regulatory Basis:

EU regulation encourages giving specific, detailed information about respiratory filter selection. Although many examples can be found where this practice is not implemented, the information is expected by some European customers. The revised Annex II to REACH, “Guide to the Compilation of Safety Data Sheets,” reinforces this expectation. The text 8.2.2.2(c) now requires:

For gases, vapours, mist or dust, the type of protective equipment to be used shall be specified based on the hazard and potential for exposure, including air-purifying respirators, specifying the proper purifying element (cartridge or canister), the adequate particulate filters and the adequate masks, or self contained breathing apparatus.

How to Specify Respiratory Protection for EU

Respirator filters sold in the EU must be coded and marked with colors for identification. The recommendation of filter type refers to these codes and their respective colors. The filter types for half and quarter mask respirators are defined in European Norm (EN) 143 as follows:

| Color | Type | Application | Class | Gas Concentration | Standard |
| --- | --- | --- | --- | --- | --- |
| brown | A | Organic gases and vapors - boiling point > 65°C | 1 2 3 | 1000 ml/m3 5000 ml/m3 10000 ml/m3 | EN 141 |
| gray | B | Inorganic gases and vapors (not CO), i.e chlorine, H2S, HCN, ... | 1 2 3 | 1000 ml/m3 5000 ml/m3 10000 ml/m3 | EN 141 |
| yellow | E | Sulfur dioxide and acidic gas and vapors | 1 2 3 | 1000 ml/m3 5000 ml/m3 10000 ml/m3 | EN 141 |
| green | K | Ammonia and organic ammonia derivatives | 1 2 3 | 1000 ml/m3 5000 ml/m3 10000 ml/m3 | EN 141 |
| brown | AX | Organic gases and vapors - boiling point <65°C - of low boiling substances groups 1 and 2 |  | gr.1: 100 ml/m3 (max 40 minutes) gr.1: 100 ml/m3 (max 20 minutes) gr.2: 1000 ml/m3 (max 60 minutes) gr.2: 5000 ml/m3 (max 20 minutes) | EN 371 |
| blue | NO | Nitrogen oxides e.g NO, NO2, NOx |  | (max 20 minutes) | EN 141 |
| red | Hg | Mercury vapors |  | (max 50 hours) | EN 141 |
| black | CO | Carbon monoxide |  |  | DIN 3181 |
| gold | Reactor P3 | Radioactive iodine |  |  | DIN 3181 |
| white | P | Particles | 1 2 3 | Low efficiency (80%) Medium efficiency (94%) High efficiency (99.95%) |  |

Useful links for reference:

http://www.msa-europe.com/uploads/tx_comaknowledgebase/Filterselection_Guide.pdf

http://www.sba.co.uk/content/doc_11.pdf

http://www.tsiinc.de/documents/AFT-003_EN%20143-appnote.pdf